## Slide 1
ADVANCED COMPUTER NETWORKS · CSE DEPARTMENT
Enterprise University Campus Network Infrastructure
Scalable, resilient, dual-stack architecture designed, implemented, and verified in Cisco Packet Tracer.
CORE STACK
802.1w Rapid-PVST · 802.1Q ROAS · RIPv2 · PAT/NAT Overload · SLAAC
SCOPE & SERVICES
3 Routers · 5 Switches · 4 Servers · 10 PCs · DNS · Intranet Web · DHCP
PRESENTER: STUDENT ID / DEPARTMENT OF CSE
Notes: Introduce the project: a complete campus network infrastructure simulated and verified in Cisco Packet Tracer. Highlight the enterprise scope: core-distribution hierarchy, 9 VLANs, dual-stack IPv4/IPv6, and centralized campus services.

## Slide 2
ARCHITECTURE HIERARCHY
Three tiers isolate departments under central control
Design Principles
Three-tier design: removes broadcast bottlenecks and isolates admin, academic, server and residential traffic.
Independent routing: at the hostel keeps guest mobile devices away from core academic databases.
Fa0
WAN 200.1.1.0/30
WAN 10.0.0.4/30 (RIPv2)
802.1Q Trunk
802.1Q Trunk
Trunk 10,60,99
Trunk 70,99
Trunk 20,30,40,99
Redundant Trunk Fa0/23 (STP BLK)
Internet Server
203.0.113.10
R-ISP Gateway
NAT/PAT Overload
R-CAMPUS Core
ROAS Gateway
R-HOSTEL
Branch Router & DHCP
SW-HOSTEL
VLAN 50 & 80
AP-HOSTEL
SSID: CAMPUS-WIFI (Port 0)
SW-CORE
Rapid-PVST Root Bridge
SW-ADMIN
Admin & Security
SW-SERVER
Web & DNS Farm
SW-ACADEMIC
CSE, IoT & Library
Notes: Walk through the three-tier hierarchy: Core, Distribution, and Access. Highlight the separation between the academic core and the residential hostel branch router to isolate mobile client broadcasts.

## Slide 3
PHYSICAL INFRASTRUCTURE
Layer 1: every link has a defined cable and role
Link | Interfaces · cable type · role
ISP WAN | R-ISP Gi0/0 to R-CAMPUS Gi0/0 · Cross-over · Public edge, 200.1.1.0/30
Hostel WAN | R-CAMPUS Gi0/2 to R-HOSTEL Gi0/0 · Cross-over · Interconnect, 10.0.0.4/30
Campus uplink | R-CAMPUS Gi0/1 to SW-CORE Fa0/1 · Straight-through · 802.1Q trunk for VLANs 10,20,30,40,60,70,99
Hostel uplink | R-HOSTEL Gi0/1 to SW-HOSTEL Gi0/1 · Straight-through · Trunk for VLANs 50,80,99
Core distribution | SW-CORE to SW-ADMIN/ACADEMIC/SERVER · Cross-over · 802.1Q trunks
Redundant link | SW-ADMIN Fa0/23 to SW-ACADEMIC Fa0/23 · Cross-over · Standby managed by Rapid-PVST
Access point | AP-HOSTEL Port 0 to SW-HOSTEL Fa0/11 · Straight-through · Port 0 is wired Ethernet; Port 1 is the 2.4GHz radio
Notes: Explain physical layer selection: DTE-to-DTE links (like router-to-router and switch-to-switch) utilize cross-over cabling in Packet Tracer, while router-to-switch and host links use straight-through cabling.

## Slide 4
Nine VLANs enforce strict broadcast boundaries
Each VLAN gets its own IPv4 /24 (gateway .1) and IPv6 /64 (gateway ::1), 2001:db8:acad:<VLAN>::/64. VLAN 99 management is IPv4-only, out-of-band, on switch SVIs.
VLAN 10 · Admin 192.168.10.0/24 2001:db8:acad:10::/64 SW-ADMIN Fa0/1-3
VLAN 20 · CSE Academic 192.168.20.0/24 2001:db8:acad:20::/64 SW-ACADEMIC Fa0/1-2
VLAN 30 · IoT & Research 192.168.30.0/24 2001:db8:acad:30::/64 SW-ACADEMIC Fa0/6-8
VLAN 40 · Library 192.168.40.0/24 2001:db8:acad:40::/64 SW-ACADEMIC Fa0/11
VLAN 50 · Hostel Wired 192.168.50.0/24 2001:db8:acad:50::/64 SW-HOSTEL Fa0/1-2
VLAN 60 · Security 192.168.60.0/24 2001:db8:acad:60::/64 SW-ADMIN Fa0/11-12
VLAN 70 · Server Farm 192.168.70.0/24 2001:db8:acad:70::/64 SW-SERVER Fa0/1-2
VLAN 80 · Hostel Wi-Fi 192.168.80.0/24 2001:db8:acad:80::/64 SW-HOSTEL Fa0/11 (AP uplink)
VLAN 99 · Management 192.168.99.0/24 n/a (IPv4 out-of-band) Switch SVIs (SW-CORE to SW-HOSTEL)
Notes: Note how VLAN IDs directly align with third-octet IPv4 addressing and fourth-hextet IPv6 addressing for administrative clarity. VLAN 99 is dedicated solely to switch SVIs for out-of-band management.

## Slide 5
LAYER 2 & INTER-VLAN ROUTING
Router-on-a-stick and Rapid-PVST give fast, loop-free switching
802.1Q Router-on-a-Stick (ROAS)
One physical trunk interface (R-CAMPUS Gi0/1) carries tagged frames across 7 logical subinterfaces:
802.1w Rapid-PVST Spanning Tree
Root Primary: SW-CORE forced as root bridge via priority 24576.
Loop Resolution: Redundant cross-over link between SW-ADMIN Fa0/23 and SW-ACADEMIC Fa0/23.
Blocking State: Because SW-ACADEMIC has the lower base MAC address, SW-ADMIN Fa0/23 transitions to Alternate Blocking.
Sub-second Failover: Proposal-agreement handshakes bypass 802.1D listening/learning delays.
Notes: Detail how ROAS multiplexes multiple VLANs across a single gigabit link to R-CAMPUS, while Rapid-PVST maintains sub-second reconvergence if the primary distribution links fail.

## Slide 6
DYNAMIC ROUTING & PROPAGATION
RIPv2 discovers routes and passes down a default route
Routing Characteristics
Classless operation: version 2 with no auto-summary stops contiguous /24 networks from collapsing into invalid /16 Class C boundaries.
Subinterface binding: Explicit network statements bind routing updates to the ROAS subinterfaces without needing separate physical ports.
Deterministic exit: All outbound packets from academic and hostel departments resolve to R-CAMPUS then traverse R-ISP via PAT.
Notes: Explain why no auto-summary is mandatory in RIPv2: without it, subnets of 192.168.0.0/16 collapse into classful boundaries. Show the propagation flow of the 0.0.0.0/0 default route.

## Slide 7
WIRELESS & CLIENT ONBOARDING
Students join Wi-Fi and get an address with zero configuration
01
1. Access Point Radio
AP-HOSTEL: 2.4 GHz channel 6, SSID CAMPUS-WIFI, secured with WPA2-PSK (AES), key Campus@123.
02
2. Central DHCP Lease
R-HOSTEL Pool WIFI: 192.168.80.0/24. Excluded range .1–.20 reserves gateway .1 and AP uplink.
03
3. Instant Verification
Laptops auto-negotiate DORA, lease 192.168.80.21+, and configure DNS 192.168.70.11 to reach intranet portal.
Notes: Describe student user journey: mobile and laptop clients associate with the WPA2-PSK SSID on AP-HOSTEL, lease their IP from R-HOSTEL's local DHCP server, and immediately resolve campus services.

## Slide 8
EDGE TRANSLATION & CORE SERVICES
PAT shares one public IP; local DNS and web serve the campus
PAT / NAT overload on R-ISP
Inside Gi0/0, outside Gi0/1. All 192.168.0.0/16 hosts translate to 203.0.113.1 via Layer 4 ports.
Inside Local | Inside Global
192.168.50.11:1028 | 203.0.113.1:1028
Confirmed with show ip nat translations.
Intranet web and DNS
DNS 192.168.70.11: www.campus.local maps to 192.168.70.10.
Web server 192.168.70.10 hosts the intranet portal over HTTP/HTTPS for every department.
Notes: Show how PAT conserves public IPv4 addresses while providing full egress to the simulated internet server at 203.0.113.10. Emphasize that internal queries for www.campus.local stay local to the server farm.

## Slide 9
IPv6 runs alongside IPv4 with no disruption
2001:db8:acad::/48
Split into /64s matching VLAN IDs (Admin 10, CSE 20, Servers 70).
ipv6 unicast-routing
On all routers; IPv4 configs untouched.
SLAAC
R-HOSTEL sends Router Advertisements on VLAN 80; laptops self-configure with no DHCPv6.
Dual-stack pings
100% ICMPv6 success across WAN routers and inter-VLAN subinterfaces.

## Slide 10
All 16 acceptance tests passed; next up is redundancy and security
Verified (16/16)
Inter-VLAN routing across Admin, CSE, IoT, Library, Security and Servers, 0% loss
Cross-router RIPv2 peering, Hostel-PC1 to Admin-PC1
DNS resolution of www.campus.local and intranet page loading
Live NAT/PAT translations on R-ISP to 203.0.113.10
Rapid-PVST root on SW-CORE, blocking port on SW-ADMIN
End-to-end dual-stack IPv6 communication
Roadmap
HSRP/VRRP for first-hop redundancy
Migrate RIPv2 to multi-area OSPFv2/OSPFv3
Stateful firewalls and departmental ACLs
Notes: Summarize results: all 16 acceptance test criteria were satisfied in Cisco Packet Tracer. Outline next steps for production deployment, including HSRP for gateway redundancy and migration from RIPv2 to multi-area OSPF.